## Slide 1: ECE477 MIDTERM DESIGN REVIEW: TEAM # 2
Andrew Hall
Team Lead
Chris Miotto
Hardware Lead
Matt Ghera
Software Lead
Braden Kirkendall
Systems Lead

## Slide 2: OUTLINE
Project Overview
Major Components
Block Diagram
Packaging Design
Electrical Schematic
PCB Layout
Prototyping Progress
Software Development Status
Project Timeline
Questions
Speaker: Andrew

## Slide 3: PROJECT OVERVIEW
Project Description - Part 1
MOUSE is a mobile surveillance robot intended for indoor use, in corporate office or residential environments.
There will be a large 18V battery allowing MOUSE to perform surveillance overnight without needing to have its battery replaced. When the battery does die, it will need to be recharged manually.
MOUSE will also have a custom circuit to step down the 18V from the battery to 5V for motors, sensors and ICs, as well as 5V to 3.3V for the microprocessor.
Powered by 4 motors, each controlling its own wheel for mobility. Will have variable speed control through the use of PWM signals.
Original Vision of Final MOUSE Design
Speaker: Braden
Notes: In this section provide a concise description of your project (you should start with your Project Description from your team website and then elaborate). What is it? What will it do? What differentiates it from similar projects and prior art? Include a relevant picture of your project or “artist rendering” of the completed project.

## Slide 4: PROJECT OVERVIEW
Project Description - Part2
MOUSE will have PIR sensors on all four sides, allowing for the detection of movement.
Viewable UI on a webpage to use MOUSE movement controls and display if any objects have been detected.
MOUSE and the web interface will send data wirelessly through WiFi via a web server.
.
Current Iteration of MOUSE webpage UI
Speaker: Braden
Notes: In this section provide a concise description of your project (you should start with your Project Description from your team website and then elaborate). What is it? What will it do? What differentiates it from similar projects and prior art? Include a relevant picture of your project or “artist rendering” of the completed project.

## Slide 5: PROJECT OVERVIEW
Project Description - Stretch Goals
The PIR sensors may be mounted to a motor to ensure 360 degree coverage, instead of simply mounting four separate sensors to each side of MOUSE.
MOUSE can follow a predetermined path set by the user.
Top Scanning Section of MOUSE
Modified Final MOUSE Design
Speaker: Braden
Notes: In this section provide a concise description of your project (you should start with your Project Description from your team website and then elaborate). What is it? What will it do? What differentiates it from similar projects and prior art? Include a relevant picture of your project or “artist rendering” of the completed project. ***add updated image of design with stepper

## Slide 6: PROJECT OVERVIEW
Why is it Different?
Does not use a camera - no potential for security vulnerabilities in revealing proprietary information from device itself or its online dashboard
Cheaper and more abundant than existing security robots which are shown to cost upwards of $50k (SPAR)
Easily configurable to follow a certain surveillance path using the recording and playback feature
Requires minimal power usage which extends battery life
Speaker: Braden
Notes: In this section provide a concise description of your project (you should start with your Project Description from your team website and then elaborate). What is it? What will it do? What differentiates it from similar projects and prior art? Include a relevant picture of your project or “artist rendering” of the completed project.

## Slide 7: PSDRS
PSDR #1 (Hardware): An ability to control the speed of the motors with PWM signals from the microcontroller.
PSDR #2 (Hardware): An ability to step down 18.5V from the battery to 5V for circuit components on the PCB and motors using a team designed DC switching regulator.
PSDR #3 (Hardware): An ability to utilize LEDs with a daisy chained shift register circuit controlled by the microcontroller to display battery life diagnostic.
PSDR #4 (Software): An ability to display data, such as movement controls and movement detection data to a viewable UI on a webpage.
PSDR #5 (Software): An ability to control the robot by sending data wirelessly through WiFi via a web server.
Stretch PSDR:
Stretch PSDR #1: An ability to record a set path and then play back the same actions: if the robot records a path for 30 seconds, then its playback should be within 1 meter of the original pathing at all times
Stretch PSDR #2: An ability to detect movement by using a PIR sensor that is attached to an motor with an encoder. The microcontroller will control the motor direction using feedback from the encoder, and the microcontroller will read the output of the PIR sensor.
Speaker: Braden

## Slide 8: MAJOR COMPONENTS
Microcontroller
Feature | ESP32 | ESP8266 | STM32
WiFi | Yes | Yes | No
Operating Voltage (V) | 3.3 | 3.3 | 2.4-3.6
GPIO Pins (Number) | 34 | 17 | 39
Communication Protocols | SPI/I2C/UART/ADC/DAC | SPI/I2C/UART/ADC/DAC | SPI/I2C/UART/ADC/DAC
PWM Channel (Number) | 16 | 8 | 6
Clock Frequency | Dual Core - 160 MHz & 240 MHz | Single Core - 80 MHz | Single Core - 48 MHz
Price | $6-$12 | $4-$6 | $1-$4
Chosen | Yes | No | No
Performs logic on signal inputs and outputs based on its software configuration to interact with other electrical design components
Responsible for receiving signals from a web server, controlling motor operation, driving LED diagnostic data, and sending motion detection data according to software integration standards.
Speaker: Matt
Notes: Choose the major (electrical) components being utilized by your design. For each component, provide a brief description of what it is, relevant specifications, and what it will do. Also, provide a couple of alternative components and justify your choice. Examples of major components include the microcontroller, motors, wireless interfaces, power converters and regulators. Examples of relevant specifications include operating speed (uC), number of I/O (uC), stall current (motors), operating voltage, and expected current consumption.

## Slide 9: MAJOR COMPONENTS
Voltage Regulator
Steps down input voltage to a stable level for use by the electrical components in the design
Responsible for performing voltage regulation to transform 18V battery voltage to 5V for use by the motors and motor driver.
A key component in our selection of a Buck Converter is the increased efficiency and complexity to merit a PSDR.
https://circuitcellar.com/research-design-hub/basics-of-design/voltage-regulators/
Linear Voltage Regulator |  | Switching Voltage Regulator | 
Pros | Cons | Pros | Cons
Simple circuit configuration | Relatively poor efficiency | High Efficiency | More external parts required
Few external parts | Considerable heat generation | Low heat generation | Complicated design
Low Noise | Only step-down (buck) operation | Boost/buck/negative voltage operation possible | Increased noise
Speaker: Andrew
Notes: Choose the major (electrical) components being utilized by your design. For each component, provide a brief description of what it is, relevant specifications, and what it will do. Also, provide a couple of alternative components and justify your choice. Examples of major components include the microcontroller, motors, wireless interfaces, power converters and regulators. Examples of relevant specifications include operating speed (uC), number of I/O (uC), stall current (motors), operating voltage, and expected current consumption.

## Slide 10: MAJOR COMPONENTS
Motors & Motor Driver
Feature | TB6612FNG | A4990 | DRV8833
Number of Motor Channels | 2 | 2 | 2
PWM controllable | Yes | Yes | Yes
Minimum Output Voltage (V) | 4.5 | 6 | 2.7
Maximum Output Voltage (V) | 13.5 | 32 | 10.8
Peak Current Output per Channel (A) | 3 | 0.9 | 2
Max Continuous Current Output per Channel (A) | 1 | 0.7 | 1.2
Price | $4.95 | $7.95 | $9.95
Chosen | Yes | No | No
Responsible for receiving GPIO signals from the microcontroller and translating them into mechanical operation for transportation
Manages 5V motor power signal to drive wheels for locomotion with controlled speed and direction.
>1A peak current output per channel for motor stall current
>0.5A continuous current output per channel
Speaker: Braden
Notes: Choose the major (electrical) components being utilized by your design. For each component, provide a brief description of what it is, relevant specifications, and what it will do. Also, provide a couple of alternative components and justify your choice. Examples of major components include the microcontroller, motors, wireless interfaces, power converters and regulators. Examples of relevant specifications include operating speed (uC), number of I/O (uC), stall current (motors), operating voltage, and expected current consumption.

## Slide 11: MAJOR COMPONENTS
Motion Detection Sensor
Responsible for taking readings of the environment and transmitting the data back to the microcontroller
Either a digital trigger or an analog stream that needs to be processed for motion detection
A key specification is the ability to produce reliable readings with a reasonable level of sensitivity
Feature | Sonar Sensor | Ultrasonic Sensor | 360° Lidar Sensor | PIR Sensor
Measurement Distance | 7.65m | ~1m | ~12m | ~4m
Angular View Area (degrees) | 48° | 15° | 360° | 125°
Cost | $39.95 | $4.50 | $99.00 | $3.33
Sensitivity in Prototype | N/A | High | N/A | Moderate
Chosen | No | No | No | Yes
Speaker: Braden
Notes: Choose the major (electrical) components being utilized by your design. For each component, provide a brief description of what it is, relevant specifications, and what it will do. Also, provide a couple of alternative components and justify your choice. Examples of major components include the microcontroller, motors, wireless interfaces, power converters and regulators. Examples of relevant specifications include operating speed (uC), number of I/O (uC), stall current (motors), operating voltage, and expected current consumption.

## Slide 12: BLOCK DIAGRAM
Speaker: Chris
Notes: Include one or more images of your system block diagram(s) here. Block diagrams should include all relevant major parts and systems, bus widths, and interface types. Don’t forget the power network.

## Slide 13: PACKAGING DESIGN
Dimensioned CAD Model
Front View (in)
Side View (in)
Speaker: Andrew
PIR Sensor and motor
3D printed Shell
Aluminum Chassis
Rubber Wheels
Notes: Include one or more images of your packaging design here. Include relevant dimensions, label main components, and discuss how you are planning to manufacture your product packaging.

## Slide 14: ELECTRICAL SCHEMATIC
Full Schematic
Speaker: Chris
Notes: Include one or more views of your electrical schematic here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your schematics should be complete, organized, and readable.

## Slide 15: ELECTRICAL SCHEMATIC
ESP
Speaker: Chris
Notes: Include one or more views of your electrical schematic here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your schematics should be complete, organized, and readable.

## Slide 16: ELECTRICAL SCHEMATIC
ESP [cont..]
Speaker: Chris
Notes: Include one or more views of your electrical schematic here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your schematics should be complete, organized, and readable.

## Slide 17: ELECTRICAL SCHEMATIC
DC Voltage Regulator and LDO
Speaker: Andrew
Notes: Include one or more views of your electrical schematic here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your schematics should be complete, organized, and readable.

## Slide 18: ELECTRICAL SCHEMATIC
Coulomb Counter
Speaker: Andrew
Notes: Include one or more views of your electrical schematic here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your schematics should be complete, organized, and readable.

## Slide 19: ELECTRICAL SCHEMATIC
DC Motor Drivers
Speaker: Chris
Notes: Include one or more views of your electrical schematic here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your schematics should be complete, organized, and readable.

## Slide 20: ELECTRICAL SCHEMATIC
Stepper Motor
Speaker: Andrew
Notes: Include one or more views of your electrical schematic here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your schematics should be complete, organized, and readable.

## Slide 21: ELECTRICAL SCHEMATIC
Shift Registers & LEDs and PIR Sensors
Speaker: Andrew
Notes: Include one or more views of your electrical schematic here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your schematics should be complete, organized, and readable.

## Slide 22: PCB LAYOUT
Full Layout
Top 5V plane
Bottom GND plane
Debugging vias
145.9mm x 121.9mm
Speaker: Andrew
Notes: Include one or more views of your PCB Layout here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your layout should be complete, organized, and readable.

## Slide 23: PCB LAYOUT
ESP / ESP USB / USB to UART
Speaker: Chris
Notes: Include one or more views of your PCB Layout here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your layout should be complete, organized, and readable.

## Slide 24: PCB LAYOUT
DC Voltage Regulator
Speaker: Andrew
Notes: Include one or more views of your PCB Layout here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your layout should be complete, organized, and readable.

## Slide 25: PCB LAYOUT
Coulomb Counter
Speaker: Andrew
Notes: Include one or more views of your PCB Layout here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your layout should be complete, organized, and readable.

## Slide 26: PCB LAYOUT
5V to 3.3V LDO with heartbeat LEDs
Speaker: Andrew
Notes: Include one or more views of your PCB Layout here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your layout should be complete, organized, and readable.

## Slide 27: PCB LAYOUT
Shift Registers & LEDs
Speaker: Andrew
Notes: Include one or more views of your PCB Layout here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your layout should be complete, organized, and readable.

## Slide 28: PCB LAYOUT
DC Motor Control
Speaker: Chris
Notes: Include one or more views of your PCB Layout here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your layout should be complete, organized, and readable.

## Slide 29: PCB LAYOUT
PIR Sensors
Speaker: Matt
Notes: Include one or more views of your PCB Layout here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your layout should be complete, organized, and readable.

## Slide 30: PCB LAYOUT
Stepper Motor Control
Speaker: Matt
Notes: Include one or more views of your PCB Layout here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your layout should be complete, organized, and readable.

## Slide 31: PROTOTYPING PROGRESS
Prototyped
Sonar Sensor
  Unable to generate any signal output
  Likely faulty or damaged and expensive to replace
Ultrasonic Sensor
  Generally correct but high variance in input readings
  Not granular enough for our application, especially at distances more than 3 feet away from the sensor
PIR Sensor
  Much more reliable motion detection
  Easier to use as signal is preprocessed into a digital output
  Tested to work effectively until ~12ft, haven’t tested past that yet
Ultrasonic Sensor Data Log
PIR Sensor Prototyping
Speaker: Braden

## Slide 32: PROTOTYPING PROGRESS
Prototyped
Websocket Communication
  Communication between micro|server & web-UI|server
  Motion alerts, DC/stepper motor controls
  Achieved ≤1 second latency
DC Motors w/ PWM
  PWM and motor control signal generation
  Able to control output frequency and motor polarity of multiple signals simultaneously
LED Shift Register Array
  Able to control 24 individual LEDs
  Need to implement Coulomb counter as data input
Stepper Motor
  Directional control and step count measuring
  Can rotate controlled angular distances
Speaker: Matt

## Slide 33: SOFTWARE OVERVIEW
Speaker: Matt

## Slide 34: SOFTWARE OVERVIEW
Speaker: Matt

## Slide 35: SOFTWARE DEVELOPMENT STATUS
Prototyped
Websocket Communication
  overall infrastructure,
  able to store inputs/states,
  setting/reading motor direction
  setting/reading movement detection time
DC Motor Control
  PWM signal generation
  Motor Driver Testing
  Basic Socket Command Hook
LED Control
  Serial control of individual LEDs
Stepper Motor Control
  Control stepper motor direction and read the step count
Speaker: Matt
Key: Completed
In Progress

## Slide 36: SOFTWARE OVERVIEW
Prototyped
Backend Socket Communication
  Creates sockets with micro and webclients
  Defined message schema for receiving and sending data
  Broadcasts alerts to all webclient connections
  Processes data according to current state
Prototyping
Movement Recording/Playback
  Record input timings from dashboard and playback recording file with time delays and looping features
  Have working at high level but will likely need to fine-tune delays with full movement capabilities
Speaker: Matt
Key: Completed
In Progress

## Slide 37: SOFTWARE OVERVIEW
Prototyped
UI Dashboard
  Active connection status
  Manual movement/scanning mode
  Integrated directional commands
  State management of recording/playback/free roam
Speaker: Matt

## Slide 38: PROJECT TIMELINE
GANTT CHART
Speaker: Andrew

## Slide 39: 3D PRINTING
Questions?